## Slide 1: Optimal Fin Design with Volume Constraint
Jackson Emerson, McKenna Marlar, Lohit Bhatnagar, Charlie Sledz

## Slide 2: Introduction & Project Objective
Our objective is to determine which fin geometry dissipates the most heat under a fixed volume constraint: cylindrical, rectangular, and conical.
Fins are used in HVAC, electronics, and automotive applications to dissipate heat efficiently.
  Their performance depends on material, airflow, and most critically — geometry.
Results can be found through analytical calculations relating to heat dissipation and can help optimize compact thermal designs for energy efficiency.

## Slide 3: Hypothesis & Assumptions
Hypothesis:
Assumptions:
Radiation is negligible.
No internal heat generation occurs.
Steady-state heat transfer is reached.
Bottom & sides of the fin base are perfectly insulated.
1D heat flow.
Cylindrical fin will dissipate more heat per unit mass
Rectangular fin will dissipate the most heat in the given boundary box

## Slide 4: Material & Equipment Utilized in Lab
Aluminum blocks
Heater
Thermocouples
IR camera
Mill
Lathe
Insulation
Black paint
Blower box
Anemometer

## Slide 5: Fabrication
Rectangular
Cylindrical
Conical
Plate

## Slide 6: Experimental Setup
Fins machined from aluminum 6061 block with different geometries (rectangular, cylindrical, conical)
Heated from the base using an electric heater
Base and heater situated in insulation
Air flow across fin via a blower to induce forced convection
Thermocouples measure temperature at fin base and tip

## Slide 7: Experimental Setup
Blower
h, T∞
Blower
h, T∞

## Slide 8: Experimental Setup

## Slide 9: Experimental Procedure
Set up airflow
Position the blower box directly next to the fin array to simulate forced convection across the surface.
Prepare sensors
Insert thermocouples at the base and tip of the fin to record temperature differences accurately.
Configure power input
Connect a wattmeter to the powerstat, ensuring a measurable power supply.
Calculate power input
Use the wattmeter readings to determine the constant electrical power being supplied to the fin base
Connect them to LabVIEW for real-time data monitoring.

## Slide 10: Experimental Procedure
Heat the system
Activate the electrical heater and allow the system to reach steady-state conditions before taking any measurements.
Record data
Monitor and log temperature readings continuously once steady state is achieved. Confirm stability in measurements before finalizing data.
Capture visual data
Use the IR camera to take thermal images of the fin surface to visualize temperature gradients and heat dissipation patterns.
Repeat for all geometries
Perform the same procedure for each fin shape (rectangular, cylindrical, conical), maintaining identical test conditions for consistency.

## Slide 11: Schematic – Side View
qfin
Pelec
qfin
Pelec
qfin
Pelec
Rectangular
Cylindrical
Conical
2 in
1 in
qconv
qconv
qconv
qcond
qcond
qcond

## Slide 12: Schematic – Top View
Rectangular
Cylindrical
Conical
1 in
1 in

## Slide 13: Analysis Overview
Determine thermal resistance of the heated base plate
Find the heat loss through the base material to isolate the heat being transferred through the fins alone.
Calculate the convective heat transfer coefficient
Use known surface temperatures and heat input to estimate the convection coefficient between the fin surfaces and the air.
Measure the thermal resistance of each fin geometry
Using the base and tip temperatures recorded by thermocouples, calculate R(fin)
Determine fin efficiency
Compute fin efficiency η for each shape, accounting for non-ideal losses. Higher efficiency implies more heat is transferred relative to a perfectly conducting fin.

## Slide 14: Results & Overview

## Slide 15: Preliminary Analysis: Flat Plate

## Slide 16: Preliminary Analysis: Rectangular Fin

## Slide 17: Preliminary Analysis: Cylindrical Fin

## Slide 18: Preliminary Analysis: Conical Fin

## Slide 19: Preliminary Analysis: Radiation

## Slide 20: Preliminary Analysis: Summary
Configuration | ReLc | NuLc | h (W/m2K) | m (-) | Fin Efficiency
Flat Plate | 22900 | 114 | 40.5 | - | -
Rectangular | 19100 | 93.9 | 39.9 | 3.64 | 0.983
Cylindrical | 17200 | 71.0 | 33.6 | 4.72 | 0.976
Conical | 7640 | 43.0 | 45.7 | 5.51 | 0.997
Radiation confirmed to be negligible, matching our assumption

## Slide 21: Experimental Analysis: Flat Plate

## Slide 22: Experimental Analysis: Fin Procedure
General
General (cont.)
Geometry Dependent

## Slide 23: Experimental Analysis: Rectangular Fin
Cylindrical fin has similar equations, but with a different m equation

## Slide 24: Experimental Analysis: Conical Fin
Cylindrical has same m equation as conical

## Slide 25: Experimental Analysis: Summary
Configuration | Trial | Rtot (K/W) | htot (W/m2K) | hfin (W/m2K) | m (-) | qf (W)
Flat Plate | 1 | 1.33 | 130 | - | - | -
 | 2 | 1.37 | 126 | - | - | -
Rectangular | 1 | 1.16 | 103 | 25.5 | 16.4 | 4.35
 | 2 | 1.08 | 110 | 21.1 | 14.9 | 3.43
Cylindrical | 1 | 1.10 | 92.1 | 15.0 | 12.6 | 2.03
 | 2 | 1.05 | 96.8 | 33.2 | 18.7 | 3.50
Conical | 1 | 1.37 | 99.0 | 85.9 | 30.1 | 3.28
 | 2 | 1.27 | 106 | 85.9 | 30.1 | 3.06

## Slide 26: Experimental Analysis: Summary
Configuration | Trial | Fin Effectiveness | Fin Efficiency | Volumetric Efficiency (W/m3) | Mass Efficiency (W/kg)
Rectangular | 1 | 7.84 | 0.75 | 0.1326 | 0.049
 | 2 | 8.22 | 0.78 | 0.1047 | 0.039
Cylindrical | 1 | 8.30 | 0.86 | 0.0619 | 0.029
 | 2 | 6.98 | 0.74 | 0.1067 | 0.050
Conical | 1 | 1.94 | 0.91 | 0.1002 | 0.142
 | 2 | 1.94 | 0.91 | 0.0933 | 0.132
Fin effectiveness of >2 is required to justify using fins
  Conical fins are not justifiable

## Slide 27: Errors & Improvements
During Experiment:
  Tip thermocouples were taped to fins on side opposing airflow
  Part of the bottom insulation melted
  IR camera & thermocouple readings differed
  Small portions of paint chipped off
Future:
  Embedded tip thermocouples
  More durable insulation material
  Smoother fin & plate surfaces

## Slide 28: Conclusions
Configuration | Volumetric Efficiency (W/m3) | Mass Efficiency (W/kg)
Rectangular | 0.133 | 0.049
 | 0.105 | 0.039
Conical | 0.100 | 0.142
 | 0.0933 | 0.132

## Slide 29: Questions?